## Slide 1
BCM Infrastructure as Code
Multi-Environment Ansible Automation for BCM 11.0 One Repo • 6 Environments • 11 Playbooks • Explicit Commands

## Slide 2
6 Environments — One Repo
Environment | What It Is | Scale
local-lab | Your workstation — KVM VMs | 1 head + 3 nodes
az2-staging | AZ2 staging cluster | 1 CPU head + 1 GPU + few CPU
az2-staging-bmaas | BMaaS staging cluster | 1 head + 3 CPU + 1 GPU
az2-bmaas-prod | BMaaS production | 1 head + 66 DGX B200
az1-prod | AZ1 production | TBD
az2-prod | AZ2 production | TBD

## Slide 3
Repository Structure
WHERE — inventories/
Per-environment: hosts.yml + group_vars/all.yml
local-lab/ • az2-staging/ • az2-staging-bmaas/ • az2-bmaas-prod/ • az1-prod/ • az2-prod/
WHAT — playbooks/ (11 playbooks)
cluster-health • dns-config • nodegroup-config • firmware-audit • firmware-upgrade
node-lifecycle • slurm-ops • slurm-jobs • debug-bundle • bcm-config • bcm-image-mgmt
HOW — roles/ (4 reusable roles)
bcm-dns • bcm-nodegroup • bcm-health • bcm-slurm
DOCS — docs/ (7 guides)
Runbook • Concepts • DNS best practices • Operations • Install troubleshooting

## Slide 4
How to Run — Explicit Commands
Pattern:
ansible-playbook -i inventories/<ENV>/hosts.yml playbooks/<PLAYBOOK>.yml
Examples:
ansible-playbook -i inventories/local-lab/hosts.yml playbooks/cluster-health.yml
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/dns-config.yml
ansible-playbook -i inventories/az2-staging/hosts.yml playbooks/firmware-audit.yml
Dry-run (add --check --diff):
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/dns-config.yml --check --diff
Specific tags only:
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/firmware-audit.yml --tags gpu,nic

## Slide 5
All 11 Playbooks
Playbook | What It Does
cluster-health.yml | Check services, disk, memory, Slurm status
dns-config.yml | Set nameservers, search domains via cmsh
nodegroup-config.yml | Manage categories, overlays, node assignments
firmware-audit.yml | Collect BIOS, BMC, GPU, NIC firmware versions
firmware-upgrade.yml | Upgrade firmware (dry-run default, safety guards)
node-lifecycle.yml | Power, provision, drain, resume nodes
slurm-ops.yml | Slurm partition management
slurm-jobs.yml | Submit and monitor Slurm jobs
debug-bundle.yml | Collect diagnostic logs and GPU info
bcm-config.yml | Audit BCM configuration objects
bcm-image-mgmt.yml | Audit and manage software images

## Slide 6
Day-0 Operations — Initial Setup
# | Operation | Playbook | Status
1 | Health baseline | cluster-health.yml | ✅ Tested
2 | BCM config audit | bcm-config.yml | ✅ Tested
3 | Image audit | bcm-image-mgmt.yml | ✅ Tested
4 | Configure DNS | dns-config.yml | 🔲 Pending
5 | Setup node categories | nodegroup-config.yml | 🔲 Pending
6 | Provision nodes | node-lifecycle.yml | ✅ Tested
7 | Setup Slurm | slurm-ops.yml | ✅ Tested
8 | Firmware audit | firmware-audit.yml | 🔲 Pending
9 | Firmware upgrade | firmware-upgrade.yml | 🔲 Pending

## Slide 7
Day-2 Operations — Ongoing Management
# | Operation | Playbook | Frequency
1 | Health check | cluster-health.yml | Daily
2 | Debug bundle | debug-bundle.yml | On incident
3 | Node power cycle | node-lifecycle.yml | As needed
4 | Node reprovision | node-lifecycle.yml | After RMA
5 | Slurm job monitoring | slurm-jobs.yml | Daily
6 | Image update | bcm-image-mgmt.yml | On patch
7 | DNS change | dns-config.yml | On network change
8 | Category change | nodegroup-config.yml | On scale
9 | Firmware upgrade | firmware-upgrade.yml | Quarterly
10 | Firmware audit | firmware-audit.yml | Monthly

## Slide 8
Firmware Audit — firmware-audit.yml
Collects from every node:
• BIOS version → dmidecode -t bios
• BMC firmware → ipmitool mc info
• GPU driver + VBIOS → nvidia-smi --query-gpu
• NIC firmware → mlxfwmanager --query
• BCM + Slurm versions → cmsh get version
Run:
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/firmware-audit.yml
GPU only:
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/firmware-audit.yml --tags gpu
Report saved to: /tmp/firmware-audit-<env>/firmware-audit-<timestamp>.md

## Slide 9
Firmware Upgrade — Safety-First
firmware-upgrade.yml — DRY-RUN by default
1. Pre-flight → checks Slurm, aborts if jobs running
2. Drain → removes nodes from Slurm
3. Upgrade GPU → updates driver in BCM image
4. Upgrade BIOS → flashes BIOS firmware
5. Upgrade BMC → updates BMC firmware
6. Upgrade NIC → flashes Mellanox ConnectX
7. Reboot → reboots nodes, waits 120s
8. Verify → re-checks all versions
9. Resume → puts nodes back in Slurm
Apply GPU driver upgrade:
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/firmware-upgrade.yml -e fw_apply=true -e target_gpu_driver=560

## Slide 10
Image vs Overlay — What Goes Where
✅ In the Image | ✅ In the Overlay
OS base packages | /etc/resolv.conf (DNS)
NVIDIA GPU drivers | NTP servers
CUDA toolkit | LDAP client config
Container runtime | Mount points (/scratch)
Slurm client (slurmd) | SSH authorized_keys
Monitoring agents | Kernel parameters
System libs | Network bonding

## Slide 11
Promotion Flow
local-lab → az2-staging → az2-staging-bmaas → az2-bmaas-prod
1. DEVELOP on local-lab (KVM VMs on your workstation)
2. TEST on az2-staging (real hardware, small scale)
3. VALIDATE on az2-staging-bmaas (BMaaS-specific testing)
4. DEPLOY to az2-bmaas-prod (production, 66 B200 nodes)
All on main branch — no branch-per-environment
Same playbooks, different inventories:
ansible-playbook -i inventories/local-lab/hosts.yml playbooks/dns-config.yml
ansible-playbook -i inventories/az2-staging/hosts.yml playbooks/dns-config.yml
ansible-playbook -i inventories/az2-bmaas-prod/hosts.yml playbooks/dns-config.yml
Same code → different variables → different outcomes

## Slide 12
Where to Find Things
I want to... | Look at...
See environment config | inventories/<env>/group_vars/all.yml
See what a playbook does | playbooks/<name>.yml
See reusable logic | roles/<name>/tasks/main.yml
Dry-run something | Append --check --diff
Run specific tags only | Append --tags <tag1>,<tag2>
BCM concepts | docs/bcm-concepts-guide.md
DNS best practices | docs/bcm-dns-and-image-best-practices.md
Install troubleshooting | docs/bcm-install-troubleshooting.md
Copy-paste commands | docs/tested-runbook.md

## Slide 13
Testing Backlog
Priority | Playbook | Status
P0 | cluster-health.yml | ✅ Tested on local-lab
P0 | dns-config.yml | 🔲 Need nodes UP
P0 | nodegroup-config.yml | 🔲 Need nodes UP
P1 | node-lifecycle.yml | ✅ Tested on local-lab
P1 | slurm-ops.yml | ✅ Tested on local-lab
P1 | debug-bundle.yml | ✅ Tested on local-lab
P1 | firmware-audit.yml | 🔲 Need nodes UP
P1 | firmware-upgrade.yml | 🔲 Need nodes UP
P2 | bcm-image-mgmt.yml | ✅ Tested on local-lab
P2 | bcm-config.yml | ✅ Tested on local-lab
P2 | slurm-jobs.yml | ✅ Tested on local-lab

## Slide 14
What's Next
Planned Playbooks:
• burn-in-test.yml — post-RMA node validation
• ldap-config.yml — LDAP/authentication setup
• network-bonding.yml — IB/ETH bond configuration
Infrastructure:
• CI/CD pipeline (lint on PR + dry-run on merge)
• Ansible Vault for secrets management
• GPU-specific playbooks (DCGM, nvidia-smi health)
Immediate:
• Get local-lab nodes fully provisioned (PXE booting now)
• Test DNS + nodegroup playbooks on live nodes
• Fill in az1-prod and az2-prod with real IPs/hostnames